Foundations of audio unit testing
Fabio Bottarelli
27275A

---
[Speaker Notes: Mondo Cos’è JUCE]

---
“This is audio software…
… you just don't test it”
[Speaker Notes: - Timbro brillante, no > 7 - manovella suono frizzante]

---
[Speaker Notes: - Test integrazione di sistemi - paper generici - cosa ho fatto io]

---
The fastest DSP crash course possible
[Speaker Notes: premessa]

---
What is audio in the time domain?
A buffer of values between with magnitude (volume) between -1 and 1

---
DEMO
[Speaker Notes: OSCILLOSCOPIO SIN / NOISE]

---
Compressor: a testable audio device in the time domain
Dampens input if volume higher than x

---
DEMO
[Speaker Notes: COMPRESSORE su SIN]

---
What is audio in the frequency domain?
A buffer of values between 0 And 1
Audible frequencies between 20Hz and 20kHz
Move from time to freq domain with FFT:
[Speaker Notes: Cos’è la FFT]

---
DEMO
[Speaker Notes: SPETTROGRAMMA SIN / NOISE]

---
Filter: a testable audio device in the frequency domain
[Speaker Notes: È un circuito che ha come effetto passabasso]

---
DEMO
[Speaker Notes: FILTRO su SIN / NOISE]

---
End of the crash course

---
[Speaker Notes: overhead odissea]

---
Sections
[Speaker Notes: - approccio diverso a setup e teardown - viene da scrivere un test unico - non è immediata la lettura di come andranno I test]

---
Generators
[Speaker Notes: Combinatorialmente]

---
Testing a lowpass filter
[Speaker Notes: Ho scritto un filtro E dei test per esso]

---
Testing a lowpass filter
And i found a bug 😱

---
DEMO
[Speaker Notes: Discorso sulla percezione umana]

---
[Speaker Notes: Stavo usando un dry/wet non adatto]

---
BDD
SCENARIO, GIVEN, THEN, AND_*

---
Code

---
SCHUBERT, Peter J.; VITKIN, Lev; BRAUN, David. Model-based Development for Event-driven Applications using MATLAB: Audio Playback Case Study. SAE Transactions, 2007, 255-260.